## Slide 1: Remove from 2nd floor storage area in parking structure and into elevator. Unit is on rolling dolly.

## Slide 2: Move into elevator from 2nd floor parking structure lot.

## Slide 3: Move to appropriate area to set up.

## Slide 4: Remove white pole lifts and remove exterior wrap.

## Slide 5: Remove first tarp (bottom of tent). Unfold and place on ground lengthwise with black velcro at each end.

## Slide 6: With floor tarp in place, move tent into center of bottom tarp.

## Slide 7: Rotate tent so fluorescent tabs line up with entrance/exit door openings.

## Slide 8: Unloosen belly strap.

## Slide 9: Loosen yellow belly strap and pull corners to four corners of tarp.

## Slide 10: Gently take the curtains and drape over the sides of the tent. Note yellow fluorescent marker that is at top of center opening.

## Slide 11: Red strap indicates clip for corner. Align corners to prepare to raise tent.

## Slide 12: Insert lifting poles at both ends, have each person push up while other members clip outside corners to bottom tarp. Adding extra people to PUSH UP from inside helps considerably.

## Slide 13: With tent raised, lock interior clips to yellow tabs on floor tarp & clip interior side tabs together.

## Slide 14: Fully set up; note clips on floor tarp, curtains can pull back with velcro straps, windows also raise up or down with velcro.

## Slide 15: To take down, station people at 4 corners, unclip interior & exterior clips, then gently glide tent and compress. Tent will collapse easily.

## Slide 16: Compress all four corners to center, apply yellow belly band tightly.

## Slide 17: Place dolly under exterior wrap first, then lift tent unit onto dolly.

## Slide 18: Close up sides, using velcro to seal sides and top.

## Slide 19: Close up exterior wrap, tighten black exterior straps.

## Slide 20: Tighten exterior straps, insert lifting poles under straps.

## Slide 21: Return to storage unit.